| CONDITION ASSESSMENT (SUMMARY) - CUSTOMER COPY | Key |
| --- | --- |
| DATE OF ASSESSMENT | 24th November 2011 | 1 | Urgent fix required |
| OWNER |  | 2 | Needs repair for normal operation |
| MARQUE | Jaguar | 3 | Recommend for restoration reasons |
| MODEL | XJS | 4 | Optional |
| COU/CAB/CON | COU |  |  |
| ENGINE SIZE | 4.0 |  |  |
| VEHICLE REGISTRATION | Jxxx xxx |  |  |
| VIN | SAJJNAED3K182627 |  |  |
| RHD/LHD | RHD |  |  |
| PAINT CODE | CFH |  |  |
| TRIM CODE | AEE |  |  |
| MILEAGE | 86017 |  |  |
| Exterior Panels, Lights, Wheels & Tyres | Observations | Other Comments | Recommendations |
| RHF Wing | Dented, | Corner near headlamp | 3 |
| RHF Chrome | Surface Rust, | Very small bubble | 4 |
| RHF Wheel Rim | Corroded, | 17" Drivenman 11 spoke. Minor corrosion | 4 |
| RHF Tyre | Worn, | 10% (235 50 17 Eagle F1) |  |
| RHF Door | Dented/Dimpled, Scratched | Minor | 3 |
| RHF Door Seal | . | Leaking water into footwell | 2 |
| RH Sill | Penetrating Rust, Surface Rust, | Minor bubble rear | 3 |
| RH Floorpan | Penetrating Rust | Moderate at seat belt mount | 3 |
| RHR Wing | Scratched | Minor | 3 |
| RHR Tyre | Worn, | 10% |  |
| LHR Light Assembly | . | Condensation |  |
| Rear Valance | Penetrating Rust, | Significant rust in RH tunnel | 3 |
| Rear Centre Chrome | Discoloured | Minor fading | 4 |
| Boot Lid | Scratched | V minor | 4 |
| Roof / Hood | . | Minor scratches | 4 |
| LHR Chrome | Bent, | Minor, on corner | 3 |
| LHR Wing | Surface Rust, Scratched | Bubble at rear sill join; scrapes on arch lip | 3 |
| LHR Wheel Rim | Corroded, | Minor |  |
| LHR Tyre | Worn, | 10% |  |
| Petrol Cap | . | Moderate |  |
| LHF Door | Dented/Dimpled, | Very minor |  |
| LHF Door Seal | PerishedDamaged/displaced | Leaking water onto footwell | 2 |
| LH Sill End | . | Minor surface rust |  |
| LH Floorpan | Penetrating Rust | Wet from inside. Fungus. Moderate rust at seatbelt mount | 2 |
| LHF Wing | Scratched | Minor | 4 |
| LHF Tyre | Worn, | 0.1 |  |
| LHF Bumper Rubber | Grazed | Minor | 4 |
| LHF Bumper Chrome | Discoloured | Minor | 4 |
| Bonnet | Stonechips | Minor | 4 |
| Front Lower Panel | Surface Rust | Moderate | 4 |
| Front Centre Chrome | Penetrating Rust, | One deep bubble | 3 |
| Steering / Suspension / Brakes - Quality | Observations | Other Comments | Recommendations |
| Top Inner Wishbone Bushes RH | Worn, | Bad | 3 |
| Lower Inner Wishbone Bushes RH | Worn, Perished | Moderate | 3 |
| ARB Link RH | Rusty |  | 3 |
| ARB Link Bush RH | Perished |  | 3 |
| Front Spring RH | . | Looks much newer than left |  |
| Front Brake Disc RH | 5% Rusty | 5% rusted. Ok |  |
| Front Brake Pads RH | 50% Worn | 50% worn |  |
| Top Inner Wishbone Bushes LH | Worn, | Bad | 3 |
| Lower Inner Wishbone Bushes LH | Perished | Moderate | 3 |
| ARB Link LH | Rusty |  |  |
| ARB Link Bush LH | Perished | Moderate | 3 |
| Front Spring LH | . | Rusty |  |
| Front Brake Disc LH | . | 5% rusty |  |
| Front Brake Pads LH | 60% Worn | 60% worn |  |
| Front Subframe 'O' Mounts | Distorted |  | 4 |
| Front Subframe 'V' Mounts | Perished, Separating, | Medium | 3 |
| Steering Rack | Bushes Worn |  | 2 |
| Rear Subframe Mounting Bushes | Perished | Moderate | 3 |
| Rear Dampers RH | . | Replaced |  |
| Rear Brake Disc RH | 10% Rusty | 10% rusted |  |
| Rear Brake Pads RH | 10% Worn | 10% worn |  |
| Rear Dampers LH | . | Replaced |  |
| Rear Brake Disc LH | 5% Rusty | 5% rusty |  |
| Rear Brake Pads LH | 10% Worn |  |  |
| Handbrake cables | . | Handbrake poor | 2 |
| Underside - Other | Observations | Other Comments | Recommendations |
| Exhaust System | Original, |  | 3 |
| Under Bonnet | Observations | Other Comments | Recommendations |
| Brake Fluid | 2% Water | 2% water; just ok | 3 |
| Coolant Hoses | Leaking, | Top & bottom replaced; others original and swelling.Leak at upper water pump union | 2 |
| Engine Temperature | . | Too cold. Stuck thermostat | 2 |
| Oil Leak | Cam Cover Leak, Timing Cover Leak, | Upper timing chain tensioner gasket; cam cover; cylinder head gasket | 3 |
| PAS | Hose Leak, Tower Seal Leak, | High pressure hose & rack. Moderate | 2 |
| Inner wing | Rusty | Holes at damper mounts | 3 |
| Electrical | Observations | Other Comments | Recommendations |
| Aerial | Stuck |  | 3 |
| Dash Instruments - Temperature | Wrong reading |  |  |
| Interior, ICE & Comfort | Observations | Other Comments | Recommendations |
| AirCon | LH Blower Inoperative, No Cool | Gas has leaked away. Possible small leak at shaft seal. LH blower only works on high speed | 2 |
| Carpets | Damp, Damaged, Requires deep clean | Fungus growing LHF | 3 |
| Leather quality - Driver's Seat | Worn, Requires deep clean | Moderate wear | 3 |
| Other Items | Observations | Other Comments | Recommendations |
| Valve caps seized | . | Valves need to be replaced | 2 |
| Screen sealing probably poor giving internal damp | . | Screen to come out, surround repaired, screen re-sealed | 3 |
| RH seat back tilt inop | . | Control unit has suffered from damp | 2 |
| LH seat all motion inop | . | Control unit has suffered from damp | 2 |
| Temp gauge intermittent | . | New gauge required | 2 |
| Bonnet struts weak | . | Replacement required | 3 |
| Engine worn at main bearings - clanks on start | . | Nothing to be done short of new engine. Condition not very serious | 4 |